| RILEM TG2 – Compaction Protocol Template/ Questionnaire Answer questions that apply to your method Add additional information that you feel is missing |
| --- |
|  | General Information: |  |
| 1 | What is the compactor type? What are any other names or aliases? | Rolling Wheel Compactor: Sidewalk Compactor; Double Wheel Steel Roller |
| 2 | Generally describe the laboratory compactor. How does it work? Describe any technical terminology used specifically with this equipment | Rolls over loose mix that is placed into a fixed volume mold insert until the mix is entirely contained within the mold. |
| 3 | What documents (standard or in-house specifications) are referenced for the use of this machine? | AASHTO Provisional Standard PP3-94, plus in house procedure reference |
| 4 | Provide any information on the Precision and Bias of this procedure. | None to date. Density of specimens is calculated to confirm compliance |
| 5 | Provide several digital photos of the compactor. |  |
| 6 | What do you like about this method? | Representative of field method |
| 7 | What do you dislike about this method? | Large and cumbersome |
|  | Specimen: |  |
| 8 | Describe the shape, size and weight of the specimens produced. | Trapezoidal |
| 9 | How do you select compaction temperature? | Based on binder manufacturer info |
| 10 | What is the compaction temperature? | Generally 135-150C |
| 11 | How long is the conditioning temperature applied? | 2 hours |
| 12 | Are molds preheated? To what temperature? What other tools, etc. are preheated? | Yes, molds are preheated with infrared lighting |
| 13 | How long does the compaction process take? | 20± minutes per ingot |
|  | Procedure for preparing the sample: |  |
| 14 | What is the general procedure for compacting samples? | 50 passes with the compactor, or until the mix is completely within fixed volume |
| 15 | What are the settings required to compact the sample? Pressure or load applied to sample Angles if applicable Number of passes or gyrations | The compactor weighs about 2000 pounds and we add another 1000 pounds. The number of passes is 50 unless more is required. |
| 16 | Is a pre-inspection of equipment required? (molds – clean, serviceable, etc) | Yes, molds are cleaned after use and non-stick coating is applied before usage |
| 17 | What is the procedure for loading the molds? Is paper (or water)used to prevent material from bonding to plates How are molds loaded? (rodding, tamping, troweling) | We use water with surfactant (light soap) within the mold, and/or dust if necessary to prevent bonding. Loose material is rodded approx. 40 times total in two lifts |
|  | Compacted sample |  |
| 18 | What measurements can be taken of the sample? Sample height Pressure readings Counters for passes and gyrations | Specimen Dimensions Final weight Bulk Density (Air voids) of cut specimens |
| 19 | How are the measurements recorded? |  |
| 20 | How is the sample removed from the compactor and mold? (post-compaction activities) | A mold insert is remove and turned upside down |
| 21 | How are the volumetric properties determined? | N/A |
| 22 | How is unit mass and density calculated? | Using AASHTO T166, T209, T275 |
| 23 | How do you characterize properties of the specimen? | Binder/mix type, binder content, gradation, target air voids, |
| 24 | Is a graphical presentation (plot) generated? | NO |